## Slide 1
MGS 723: Geodynamics
Class 14: Finite Differences II
Content mainly sourced from Becker and Kaus, Numerical Geodynamics

## Slide 2
Today: Solving the heat equation using Finite Differences

## Slide 3
Recap: Discretizing derivatives
1st derivative (central difference, second order accuracy)
2

## Slide 4
Recap: Discretizing derivatives
1st derivative (central difference, second order accuracy)
1st derivative (forward difference, first order accurate)
2

## Slide 5
Recap: Discretizing derivatives
2nd derivative (central difference, second order accuracy)
i
i+1
i+2
i-1
i-2
fi
fi-1
fi+1
1st derivative (central difference, second order accuracy)
2
2

## Slide 6
The second derivative with variable k can be written as following (to second order):
Recap: Variable coefficients
2

## Slide 7
Discretizing the heat conduction equation
1-D, time dependent, conduction equation
= density
= heat capacity
= thermal conductivity
Assuming constant , , and , this simplifies to:
= /(thermal diffusivity [m2s-1]

## Slide 8
Discretizing the heat conduction equation
1-D, time dependent, conduction equation
= density
= heat capacity
= thermal conductivity
Assuming constant , , and , this simplifies to:
= /(thermal diffusivity [m2s-1]
Goal: use FD to solve for T(x,t) assuming some initiation T(x,0)
1st step: Discretize the equation using the points on a grid.

## Slide 9
Discretizing the heat conduction equation
1-D, time dependent, conduction equation
= density
= heat capacity
= thermal conductivity
Assuming constant , , and , this simplifies to:
= /(thermal diffusivity [m2s-1]
Goal: use FD to solve for T(x,t) assuming some initiation T(x,0)
1st step: Discretize the equation using the points on a grid.
= the time index (1 to nt);
i = the spatial index (1 to nx)
The time-derivative (left hand-side): (forward FD)
temperature at the next timestep at grid point i
temperature at the current timestep at grid point i

## Slide 10
Discretizing the heat conduction equation
1-D, time dependent, conduction equation
= density
= heat capacity
= thermal conductivity
Assuming constant , , and , this simplifies to:
= /(thermal diffusivity [m2s-1]
Goal: use FD to solve for T(x,t) assuming some initiation T(x,0)
1st step: Discretize the equation using the points on a grid.
The spatial-derivative (right hand-side): (central FD)
= the time index (1 to nt);
i = the spatial index (1 to nx)
The time-derivative (left hand-side): (forward FD)

## Slide 11
Discretizing the heat conduction equation
So, discretizing the equation:

## Slide 12
Discretizing the heat conduction equation
So, discretizing the equation:
Rearranging so that the temperature of the next time step (n+1), which we solve for, is on the left-hand side. On the right-hand side is the temperature of the current step, which we know.

## Slide 13
Discretizing the heat conduction equation
So, discretizing the equation:
Rearranging so that the temperature of the next time step (n+1), which we solve for, is on the left-hand side. On the right-hand side is the temperature of the current step, which we know.
Because the spatial derivative was discretized at the current time (n), this is an example of the Explicit finite difference method.
I.e., we know the temperature at the current time-step (n) and use that to compute it at the next step (n+1)

## Slide 14
Because the spatial derivative was discretized at the current time (n), this is an example of the Explicit finite difference method.
I.e., we know the temperature at the current time-step (n) and use that to compute it at the next step (n+1)
Discretizing the heat conduction equation
So, discretizing the equation:
Rearranging so that the temperature of the next time step (n+1), which we solve for, is on the left-hand side. On the right-hand side is the temperature of the current step, which we know.
What is the accuracy of this solution?

## Slide 15
Because the spatial derivative was discretized at the current time (n), this is an example of the Explicit finite difference method.
I.e., we know the temperature at the current time-step (n) and use that to compute it at the next step (n+1)
Discretizing the heat conduction equation
So, discretizing the equation:
Rearranging so that the temperature of the next time step (n+1), which we solve for, is on the left-hand side. On the right-hand side is the temperature of the current step, which we know.
What is the accuracy of this solution?
1st order in , 2nd order in

## Slide 16
Discretizing the heat conduction equation
Explicit finite differences
1st order in ,
2nd order in

## Slide 17
Discretizing the heat conduction equation
Explicit finite differences
1st order in ,
2nd order in
Explicit finite differences (as opposed to implicit finite differences) are relatively simple to set up as only one temperature solution needs to be stored (i.e., the previous one, here T n)

## Slide 18
Discretizing the heat conduction equation
Explicit finite differences
1st order in ,
2nd order in
Explicit finite differences (as opposed to implicit finite differences) are relatively simple to set up as only one temperature solution needs to be stored (i.e., the previous one, here T n)
But a major drawback is that the explicit FD solution is only conditionally stable. If the following stability criterion is not satisfied, the solution oscillates wildly (“blows up”):
(Criterion can be derived from a von Neumann stability analysis of the PDE)
Notes: However, phys- ically, the stability condition eq. (4.41) means that the maximum time step needs to be smaller than the time it takes for an anomaly to diffuse across the grid (nodal) spacing ∆x (cf. diffusion time in sec. 3.3).

## Slide 19
Exercise #3: Conductive cooling of a dike in 1-D
The physical problem

## Slide 20
Exercise #3: Conductive cooling of a dike in 1-D
The physical problem
The numerical grid
The discretized equation (explicit FD method)

## Slide 21
Exercise #3: Conductive cooling of a dike in 1-D
Explicit FDs
Code stencil:

## Slide 22
Discretizing the heat conduction equation: Implicit FDs
Because the spatial derivative is evaluated at the new time-step (n+1), this is an example of the Implicit finite difference method.

## Slide 23
Discretizing the heat conduction equation: Implicit FDs
Rearranging so known terms are on the right (i.e., current temperatures), unknown terms are on the left (i.e., next step temperatures)
with
Because the spatial derivative is evaluated at the new time-step (n+1), this is an example of the Implicit finite difference method.

## Slide 24
Discretizing the heat conduction equation: Implicit FDs
Because the spatial derivative is evaluated at the new time-step (n+1), this is an example of the Implicit finite difference method.
Rearranging so known terms are on the right (i.e., current temperatures), unknown terms are on the left (i.e., next step temperatures)
We no longer have an explicit relationship for T n+1. Rather, we must solve a linear set of equations, which can be written as:
with
Old (n) temperatures that form right-hand side of above equation
New (n+1) temperatures. To solve for!
Mainly coefficients of linear equations (here, -s and 1+2s) and to deal with boundary conditions.

## Slide 25
Discretizing the heat conduction equation: Implicit FDs

## Slide 26
Discretizing the heat conduction equation: Implicit FDs
In order:

## Slide 27
Discretizing the heat conduction equation: Implicit FDs
In order:
Note: sets constant T boundary conditions

## Slide 28
Discretizing the heat conduction equation: Implicit FDs
In order:
A is a “sparse” matrix (most off-diagonals are zero). Can be exploited numerically

## Slide 29
Discretizing the heat conduction equation: Implicit FDs
In order:
Returning to the stability issue…
In contrast to the explicit solution, the implicit FD solution is unconditionally stable (i.e., no “blow ups”). A major advantage!
This doesn’t mean it will always be accurate (again, it’s 1st order in , 2nd order in ).

## Slide 30
Exercise #3: Conductive cooling of a dike in 1-D
Implicit FDs
Code stencil:

## Slide 31
With variable coefficients
Constant diffusivity case (as before):
where

## Slide 32
With variable coefficients
Constant diffusivity case (as before):
Spatially variable conductivity, i.e.:
where

## Slide 33
With variable coefficients
Constant diffusivity case (as before):
Spatially variable conductivity, i.e.:
where
where and are coefficients to the
left and right of i, respectively

## Slide 34
Different discretization schemes
Explicit FD discretization
Implicit FD discretization
Crank-Nicholson FD
discretization
O(, O(
O(, O(

## Slide 35
Different discretization schemes
Crank-Nicholson FD
discretization
O(, O(
Crank-Nicholson combines the explicit and implicit spatial derivatives (i.e., is “partially implicit”) to get the best accuracy

## Slide 36
Modeling overview
Finite difference method
http://www-udc.ig.utexas.edu/external/becker/Geodynamics557.pdf
Numerical geodynamics resources
Today:
Sects. 4.2-4.4

## Slide 37
Take homes:
  FD schemes can be explicit, implicit, partially implicit.
  For the heat conduction equation:
    Explicit: Spatial derivative(s) compute for previous time-step. (Easy to implement, but only conditionally stable.)
    Implicit: Spatial derivative(s) compute for next time-step. (Trickier to implement, unconditionally stable)
    Partially: A mixture. (Also, tricky to implement, but high accuracy in time).
  For any FD difference scheme you use, be sure to know: What are the conditions for stability? What is the accuracy as f(, ,